## Slide 1: Distributed Arithmetic ECE 4740/5740 Professor Hanna

## Slide 2: MAC Operations
Multiply and accumulate operation

## Slide 3: MAC Operations
A=[A1, A2, …, Ak] is a matrix of previously determined values (i.e. filter coefficients)
x=[x1, x2, …, xk] is a matrix of inputs
Each Ak has M-bits and xk has N-bits

## Slide 4: MAC Operations
Multi-bit AND gate
Registers to hold sum of partial products
Shift registers
Each scaling accumulator calculates Ai X xi
Shift right
Adder/Subtractor

## Slide 5: Distributed Arithmetic
  xk is an N-bit normalized two’s complement number
  | xk | < 1
  xk : {bk0, bk1, bk2……, bk(N-1) }
    where bk0 is the sign bit
  We can express xk as
  Substituting (2) in (1),
(1)
(2)

## Slide 6: Distributed Arithmetic
(3)

## Slide 7: Distributed Arithmetic
(3)

## Slide 8: Distributed Arithmetic

## Slide 9: Distributed Arithmetic

## Slide 10: Distributed Arithmetic
Originally
Bit Level Rearrangement
K cycles
# Taps
N cycles
# bits

## Slide 11: Distributed Arithmetic
has only 2K possible values i.e.
These can be pre-calculated for all possible values of b1n b2n …bKn
Store these in a look-up table of 2K words addressed by K-bits i.e. b1n b2n …bKn

## Slide 12: Distributed Arithmetic
Let number of taps K=4
The fixed coefficients are A1 =0.72, A2= -0.3, A3 = 0.95, A4 = 0.11
We need 2K = 24 = 16-words ROM

## Slide 13: Distributed Arithmetic
b1n | b2n | b3n | b4n | Contents
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | A4=0.11
0 | 0 | 1 | 0 | A3=0.95
0 | 0 | 1 | 1 | A3+ A4=1.06
0 | 1 | 0 | 0 | A2=-0.30
0 | 1 | 0 | 1 | A2+ A4= -0.19
0 | 1 | 1 | 0 | A2+ A3=0.65
0 | 1 | 1 | 1 | A2+ A3 + A4=0.75
1 | 0 | 0 | 0 | A1=0.72
1 | 0 | 0 | 1 | A1+ A4=0.83
1 | 0 | 1 | 0 | A1+ A3=1.67
1 | 0 | 1 | 1 | A1+ A3 + A4=1.78
1 | 1 | 0 | 0 | A1+ A2=0.42
1 | 1 | 0 | 1 | A1+ A2 + A4=0.53
1 | 1 | 1 | 0 | A1+ A2 + A3=1.37
1 | 1 | 1 | 1 | A1+ A2 + A3 + A4=1.48
The fixed coefficients are A1 =0.72, A2= -0.3,
A3 = 0.95, A4 = 0.11

## Slide 14: Decomposing the ROM
Requires additional adder to the sum the partial outputs

## Slide 15: Digital Frame Grabber

## Slide 16: Image Filter N x N
Filter Rotated 180 Degrees
Digital Image Filter Implementation

## Slide 17: Image Filter N x N
Threshold +

## Slide 18: Image Filter N x N

## Slide 19: Image Filter N x N

## Slide 20: Distributed Arithmetic

## Slide 21: MACs vs. Distributed Arithmetic
Filter (# taps) | Slices | LUTs | FFs
6 | 264 | 213 | 509
10 | 474 | 406 | 916
13 | 386 | 334 | 749
20 | 856 | 705 | 1650
28 | 1294 | 1145 | 2508
41 | 2154 | 1719 | 4161
61 | 3264 | 2591 | 6303
119 | 6009 | 4821 | 11551
151 | 7579 | 6098 | 14611
Filter (# taps) | Slices | LUTs | FFs
6 | 524 | 774 | 1012
10 | 781 | 1103 | 1480
13 | 929 | 1311 | 1775
20 | 1191 | 1631 | 2288
28 | 1774 | 2544 | 3381
41 | 2475 | 3642 | 4748
61 | 3528 | 5335 | 6812
119 | 6484 | 9754 | 12539
151 | 8274 | 12525 | 15988
Filter Implementation Using Add and Shift Method
Filter Implementation Using Non-DA (MACs)
Virtex II Pro

## Slide 22: MACs – Distributed Arithmetic
Quadrature Mirror Filter, Al-Haj, et. al.